## Slide 1: Plasma based Integrated On-chip Antenna
Hasan T. Abbas and Robert D. Nevels
2016 IEEE International Symposium on Antennas and Propagation and North American Radio Science Meeting, Fajardo, Puerto Rico, Jun 26 - Jul 1 2016
Dept. of ECEN, Texas A&M University, College Station, TX, USA

## Slide 2: Outline
  2D Plasmonic materials
  Dyakonov-Shur Instability
  Radiative Emission
  Radiation Detection
  Thermal Effects
  Directivity Enhancement
  Current state-of-the-art
  Comparison with Graphene

## Slide 3: Terahertz Plasmons
Bulk
  Semiconductor Substrates
  No dispersion at terahertz or microwave frequencies
2D Electron Gas
  Semiconductor heterostructures and graphene
  Extreme sub-wavelength confinement
  Reduced circuit dimensions
e: Electron Charge
N: Electron Charge Density
m*: effective mass of electron
ε: permittivity of the medium
d: top substrate layer thickness
Notes: Owing to the difficulties in engineering Graphene in bulk and the its high cost, we focus on the 2DEG found in semiconductor heterojunction that are formed naturally in the fabrication process.

## Slide 4: Metal vs Semiconductor Plasmonics
Białek, M. and Czapkiewicz, M. and Wróbel, J. and Umansky, V. and Łusakowski, J. “Plasmon dispersions in high electron mobility terahertz detectors,” in Applied Physics Letters, 104, 263514 (2014), DOI:http://dx.doi.org/10.1063/1.4886970.
  2DEG Plasmon Dispersion Diagram at Terahertz Frequency
Nevels, R. and Abbas, H. “Optical Nanoantennas,” in Handbook of Antenna Technologies, Springer Singapore pp. 1-33, (2015)
  Surface Plasmon Dispersion Diagram for Silver/Air interface at Optical frequency
Notes: Owing to the difficulties in engineering Graphene in bulk and the its high cost, we focus on the 2DEG found in semiconductor heterojunction that are formed naturally in the fabrication process.

## Slide 5: 2D Plasmon Wavelength Reduction
At 30 GHz:
  Free-space wavelength
  Plasmonic wavelength
        *
Plasmonic wavelength nearly 250 times shorter than free space wavelength
*Andress, W. A. et al., “Ultra-Subwavelength Two-Dimensional Plasmonic Circuits,” in Nano Letters vol. 12 no. 5, pp. 2272-2277, 2012.
Notes: Owing to the difficulties in engineering Graphene in bulk and the its high cost, we focus on the 2DEG found in semiconductor heterojunction that are formed naturally in the fabrication process.

## Slide 6: The 2DEG plasmon
Semiconductor Heterostructure
  2 Dimensional Electron Gas (2DEG) formed at the heterojunction
  Junction materials have different bandgaps
  GaN/AlGaN and GaAs/AlGaAs commonly used
  High Electron Mobility Transistor (HEMT) incorporates 2DEG as a channel
  With contemporary HEMT dimensions, plasma waves are generated in the low terahertz region.

## Slide 7: 2DEG Characterization
Dielectric Constant
  Gated Region
  Ungated Region
Conductivity
e: Electron Charge
N: Electron Charge Density
m*: effective mass of electron
: Scattering time of electron transport

## Slide 8: Dyakonov-Shur Instability
  Transistor channel can become unstable when properly biased
  Asymmetric boundary conditions on the channel (source – short circuited, drain – open circuited) lead to laser-like phenomena
  Resonant amplification of plasma waves in the 2DEG leads to radiative emission
V: Voltage
v: Electron velocity
J: Current Density
L: channel length
Notes: Electron flow in a 2DEG is of ballistic nature. Means, the flow (or the current) starts to shoot in the saturation region.

## Slide 9: 2DEG: Transmission Line Model
  Plasma Oscillations described by the hydrodynamic model
k: Complex wavenumber
N: Electron Charge Density
𝜀𝑒𝑓𝑓: (𝜀1 + 𝜀2)/2
m*: effective mass of electron
: Scattering time of electron transport
w: Thickness of 2DEG
Notes: Electron flow in a 2DEG is of ballistic nature. Means, the flow (or the current) starts to shoot in the saturation region.

## Slide 10: Field Integral (TM): Gated Region
For a magnetic dipole source, in region 0:
where,
Notes: Electron flow in a 2DEG is of ballistic nature. Means, the flow (or the current) starts to shoot in the saturation region.

## Slide 11: Radiation Sensing
  Incident electromagnetic waves couple with the 2DEG plasma waves
  Enhanced plasma oscillations induce a dc voltage across the drain and source terminals.
  The detector response displays a modal behavior
Dyakonov, M.; Shur, M., "Detection, mixing, and frequency multiplication of terahertz radiation by two-dimensional electronic fluid," in Electron Devices, IEEE Transactions on , vol.43, no.3, pp.380-387, Mar 1996

## Slide 12: Thermal Effects
  Electron scattering severely dampens plasma oscillations
  Significant response only obtained at cryogenic temperatures
  2DEG Mobility
Klimenko, O. A. et al., “Temperature enhancement of terahertz responsivity of plasma field effect transistors,” in Journal of Applied Physics,112, 014506 , 2012.

## Slide 13: Directivity Enhancement
  Radiation into the semiconductor layers
  Silicon lens commonly used to focus radiation through the dielectric
Popov, V. V. et al., “Resonant excitation of plasma oscillations in a partially gated two-dimensional electron layer,” in Journal of Applied Physics,98, 033510 , 2005.
Notes: Resonant excitation of plasma oscillations in a partially gated two-dimensional electron layerPopov, V. V. and Polischuk, O. V. and Shur, M. S., Journal of Applied Physics, 98, 033510 (2005), DOI:http://dx.doi.org/10.1063/1.1954890

## Slide 14: Plasmonic Microwave Devices
  Similar to Surface Plasmon Polaritons (SPP) in the optical domain, 2D plasmons assist in extreme subwavelength confinement
  Miniaturization of transmission lines and antenna
  Cryogenic Temperature operation
Andress, W. A. et al., “Ultra-Subwavelength Two-Dimensional Plasmonic Circuits,” in Nano Letters vol. 12 no. 5, pp. 2272-2277, 2012.

## Slide 15: Conclusion
  Instability of resonant plasma waves in a 2DEG results in terahertz radiation
    On-chip antenna in the terahertz region can be designed
    Engineering of special materials displaying low loss at room temperatures required
  Resonant wavelength in a 2DEG much shorter than a metal dipole counterpart
    Antenna miniaturization

## Slide 16: Questions?