## Slide 1: Plasma based Integrated On-chip Antenna
Hasan T. Abbas and Robert D. Nevels

## Slide 2: Outline
  2D Plasmonic materials
  Dyakonov-Shur Instability
  Radiative Emission
  Radiation Detection
  Thermal Effects
  Directivity Enhancement
  Current state-of-the-art
  Comparison with Graphene

## Slide 3: Terahertz Plasmons 3D vs 2D
3D
  Found in Bulk Metals
  No dispersion at terahertz or microwave frequencies
2D
  Found in semiconductor heterostructures and graphene
  Extreme sub-wavelength confinement
  Reduced circuit dimensions
Notes: Owing to the difficulties in engineering Graphene in bulk and the its high cost, we focus on the 2DEG found in semiconductor heterojunction that are formed naturally in the fabrication process.

## Slide 4: The 2DEG plasmon
Semiconductor Heterostructure
  2 Dimensional Electron Gas (2DEG) formed at the heterojunction
  Junction materials have different bandgaps
  GaN/AlGaN and GaAs/AlGaAs commonly used
  High Electron Mobility Transistor (HEMT) incorporates 2DEG as a channel

## Slide 5: Dyakonov-Shur Instability
  Transistor channel can become unstable when properly biased
  Asymmetric boundary conditions on the channel (source – short circuited, drain – open circuited) lead to laser-like phenomena
  Resonant amplification of plasma waves in the 2DEG leads to radiative emission
Notes: Electron flow in a 2DEG is of ballistic nature. Means, the flow (or the current) starts to shoot in the saturation region.

## Slide 6: Radiative Emission
  Gated and ungated regions have different plasma frequencies
  With contemporary HEMT dimensions, plasma waves are generated in the low terahertz region.

## Slide 7: Radiation Detection
  Incident electromagnetic waves couple with the 2DEG plasma waves
  Enhanced plasma oscillations induce a dc voltage across the drain and source terminals.
  The detector response displays a modal behavior
Dyakonov, M.; Shur, M., "Detection, mixing, and frequency multiplication of terahertz radiation by two-dimensional electronic fluid," in Electron Devices, IEEE Transactions on , vol.43, no.3, pp.380-387, Mar 1996

## Slide 8: Thermal Effects
  Electron scattering severely dampens plasma oscillations
  Significant response only obtained at cryogenic temperatures
  2DEG Mobility
Klimenko, O. A. et al., “Temperature enhancement of terahertz responsivity of plasma field effect transistors,” in Journal of Applied Physics,112, 014506 , 2012.

## Slide 9: Directivity Enhancement
  Radiation into the semiconductor layers
  Silicon lens commonly used to focus radiation through the dielectric
Popov, V. V. et al., “Resonant excitation of plasma oscillations in a partially gated two-dimensional electron layer,” in Journal of Applied Physics,98, 033510 , 2005.
Notes: Resonant excitation of plasma oscillations in a partially gated two-dimensional electron layerPopov, V. V. and Polischuk, O. V. and Shur, M. S., Journal of Applied Physics, 98, 033510 (2005), DOI:http://dx.doi.org/10.1063/1.1954890

## Slide 10: Plasmonic Terahertz Devices
  Similar to Surface Plasmon Polaritons (SPP) in the optical domain, 2D plasmons assist in extreme subwavelength confinement
  Miniaturization of transmission lines and antenna
Andress, W. A. et al., “Ultra-Subwavelength Two-Dimensional Plasmonic Circuits,” in Nano Letters vol. 12 no. 5, pp. 2272-2277, 2012.

## Slide 11: 2DEG vs Graphene
2DEG
  Well-established manufacturing process
  Inherent to High Electron Mobility Transistors
  Low-cost
  Integrable
Graphene
  Difficult to engineer
  Not grown on semiconductor substrates
  Difficult to integrate
  High cost
  ‘Contamination’ diminishes the exotic characteristics

## Slide 12: Conclusion
  Instability of resonant plasma waves in a 2DEG results in terahertz radiation
    On-chip antenna in the terahertz region can be designed
    Engineering of special materials displaying low loss at room temperatures required
  Resonant wavelength in a 2DEG much shorter than a metal dipole counterpart
    Antenna miniaturization

## Slide 13: Questions?